Notation:
Registers are denoted RX where X is a number between 0 and 7 inclusive. / Named registers are as follows: / Status register: SR / Link register: LR / Stack Pointer: SP / Program Counter: PC	Flag Bits Key: - : unaffected 1 : set to 1 0 : set to 0 ? : Affected but value depends on result. / Rd – Destination Register Ra – argument register a Rb – argument register b Ka – Constant address Kd – Constant data [x] – Value contained within 'x' {x} – Location pointed too by 'x' M – The result of a mask operation on the lower 5 bits of the SR

Status Register:
Bit	Flag	Description
0	N	Negative Flag – The result of the last operation was negative.
1	Z	Zero Flag – The result of the last operation was zero.
2	O	Overflow – The previous operation caused an overflow.
3	L	Less than - the result of the previous compare operation
4	E	Equal to - the result of the previous compare operation
5	G	Greater than - the result of the previous compare operation
6	PR	Privilege Bits. These store the security privilege of the currently running code. They are configured by the kernel and from then on are handled only by hardware.
7
8	S	Supervisor mode. The Privilege bits may only be configured when this is set to 1. If set then we are running in “super user” mode.
9+		Reserved for future use.

Instruction Set:
#	OPCODE	MEMONIC	DESCRIPTION	FLAGS ALTERED	FUNCTION
00	??????	BLSLI	Logical Shift Left With Immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] << Kd
01	??????	BLSLR	Logical Shift Left With Register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] << [Rb]
02	??????	BLSRI	Logical Shift Right with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] >> Kd
03	??????	BLSRR	Logical Shift Right with Register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] >> [Rb]
04	??????	BANDI	Bitwise AND with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] ^ Kd
05	??????	BANDR	Bitwise AND with register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] ^ [Rb]
06	??????	BNADI	Bitwise NAND with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] AND Kd
07	??????	BNADR	Bitwise NAND with register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] NAND Kd
08	??????	BIORI	Bitwise inclusive OR with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] OR Kd
09	??????	BIORR	Bitwise inclusive OR with register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] OR [Rb]
10	??????	BNORI	Bitwise NOR with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] NOR Kd
11	??????	BNORR	Bitwise NOR with register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] NOR [Rb]
12	??????	BXORI	Bitwise XOR with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] XOR Kd
13	??????	BXORR	Bitwise XOR with register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] XOR [Rb]
14	??????	BNOTR	Bitwise NOT	N:? Z:? O:? L:- E:- G:-	Rd ← NOT [Ra]
15	??????	AASLI	Arithmetic shift left with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] < Kd
16	??????	AASLR	Arithmetic shift left with register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] < [Rb]
17	??????	AASRI	Arithmetic shift left with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] > Kd
18	??????	AASRR	Arithmetic shift right with register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] > [Rb]
19	??????	AADDI	Add with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] + Kd
20	??????	AADDR	Add with register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] + [Rb]
21	??????	ASUBI	Subtract with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] - Kd
22	??????	ASUBR	Subtract with register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] - [Rb]
23	??????	AMULI	Multiply with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] * Kd
24	??????	AMULR	Multiply with register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] * [Rb]
25	??????	ADIVI	Integer Divide with immediate	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] / Kd
26	??????	ADIVR	Integer Divide with register	N:? Z:? O:? L:- E:- G:-	Rd ← [Ra] / [Rb]
27	??????	MLRFI	Load to register from immediate	N:? Z:? O:- L:- E:- G:-	Rd ← {Kd}
28	??????	MLIRO	Load to register from immediate with register offset	N:? Z:? O:- L:- E:- G:-	Rd ← {Kd + [Ra]}
29	??????	MLRRO	Load to register from register with register offset	N:? Z:? O:- L:- E:- G:-	Rd ← {[Ra] + [Rb]}
30	??????	MSRAI	Store register at immediate	N:- Z:- O:- L:- E:- G:-	{Kd} ← [Rd]
31	??????	MSIRO	Store register at immediate with register offset	N:- Z:- O:- L:- E:- G:-	{Kd + [Ra]} ← [Rd]
32	??????	MSRRO	Store register at register with register offset	N:- Z:- O:- L:- E:- G:-	{[Ra] + [Rb]} ← [Rd]
33	??????	BRANI	Branch to immediate address	N:- Z:- O:- L:- E:- G:-	PC ← Kd
34	??????	BRANR	Branch to address in register	N:- Z:- O:- L:- E:- G:-	PC ← {Ra}
35	??????	BRWMI	Branch with mask to immediate address	N:- Z:- O:- L:- E:- G:-	PC ← {Ra} ? M!=0
36	??????	CALLR	Call subroutine starting add address in register. Push PC to LR	N:- Z:- O:- L:- E:- G:-	LR ← [PC]; PC ← {Ra}
37	??????	CARET	Call Return – Return from Subroutine	N:- Z:- O:- L:- E:- G:-	PC ← [LR]
38	??????	STPSH	Push register to stack. Increment stack pointer.	N:- Z:- O:- L:- E:- G:-	{SP} ← Ra
39	??????	STPOP	Pop to register from stack. Decrement stack pointer.	N:- Z:- O:- L:- E:- G:-	Rd ← {SP}
40	??????	STKLD	Load stack register to gp register	N:- Z:- O:- L:- E:- G:-	Rd ← [SP]
41	??????	STLST	Load the status register to gp register.	N:? Z:? O:- L:- E:- G:-	Rd ← [SR]
42	??????	COMPR	Compare Two Registers and set the status flags accordingly	N:? Z:? O:0 L:? E:? G:?	Perform (Ra – Rd)
43	??????
44	??????
45	??????
46	??????
47	??????
48	??????
49	??????
50	??????
51	??????
52	??????
53	??????
54	??????
55	??????
56	??????
57	??????
58	??????
59	??????
60	??????
61	??????	DEBUG	Used to access debug functionality from within the SIM	N:- Z:- O:- L:- E:- G:-
62	??????	RESET	Performs a soft reset on the processor core.	N:- Z:- O:- L:- E:- G:-	PC ← 0
63	??????	HALT	Stops all processing	N:- Z:- O:- L:- E:- G:-